## Slide 1
Measuring systems
Definitions (international)

## Slide 2
Measuring systems – Definitions

## Slide 3
OIML V 2-200

## Slide 4
OIML V 2-200
3.1
measuring instrument
device used for making measurements, alone or in conjunction with one or more supplementary devices
NOTE 1 A measuring instrument that can be used alone is a measuring system.
NOTE 2 A measuring instrument may be an indicating measuring instrument or a material measure.

## Slide 5
OIML V 2-200
3.2
measuring system
set of one or more measuring instruments and often other devices, including any reagent and
supply, assembled and adapted to give information used to generate measured quantity values within specified intervals for quantities of specified kinds
NOTE A measuring system may consist of only one measuring instrument.

## Slide 6
OIML V 2-200
3.3
indicating measuring instrument
measuring instrument providing an output signal carrying information about the value of the quantity being measured
EXAMPLES Voltmeter, micrometer, thermometer, elec-tronic balance.
NOTE 1 An indicating measuring instrument may pro-vide a record of its indication.
NOTE 2 An output signal may be presented in visual or acoustic form. It may also be transmitted to one or more other devices.

## Slide 7
OIML V 2-200
3.6
material measure
measuring instrument reproducing or supplying, in a permanent manner during its use, quantities of one or more given kinds, each with an assigned quantity value
EXAMPLES Standard weight, volume measure (sup-plying one or several quantity values, with or without a quantity-value scale), standard electric resistor, line scale (ruler), gauge block, standard signal generator, certified reference material.
NOTE 1 The indication of a material measure is its assigned quantity value.
NOTE 2 A material measure can be a measurement standard.

## Slide 8
OIML V 1
Quotes the OIML V 2-200

## Slide 9
OIML V 1
0.10
measuring instrument
device used for making measurements, alone or in conjunction with one or more supplementary devices
Note 1 A measuring instrument that can be used alone is a measuring system.
Note 2 A measuring instrument may be an indicating measuring instrument or a material measure.
[OIML V2-200:2012, 3.1]

## Slide 10
OIML V 1
0.12
measuring system
set of one or more measuring instruments and often other devices, including any reagent and supply, assembled and adapted to give information used to generate measured quantity values within specified intervals for quantities of specified kinds
Note A measuring system may consist of only one measuring instrument.
[OIML V2-200:2012, 3.2]

## Slide 11
WELMEC 8.1
Gives references to
the definitions in MID

## Slide 12
MID
Article 4
Definitons
„measuring instrument“ means any device or system with a measurement function that is covered by Article 2(1)
Directive 2014/32/EU
MI-005
Definitons
measuring System
A system that comprises the meter itself and
all devices required to ensure correct
measurement or intended to facilitate the
measuring operations
Notes: 1. „Messgerät“: jedes Gerät oder System mit einer Messfunktion,
das unter Artikel 2 Absatz 1 fällt;
Messanlage
Eine Anlage, die den Zähler und alle Einrichtungen umfasst, die erforderlich sind, um
eine korrekte Messung zu gewährleisten, oder dazu dienen, die Messvorgänge zu erleichtern.

## Slide 13
Conclusion
No clear borderline between measuring instrument
and measuring system
Both expressions are often mixed
Is it necessary to destinguish?
Notes: 1. „Messgerät“: jedes Gerät oder System mit einer Messfunktion,
das unter Artikel 2 Absatz 1 fällt;
Messanlage
Eine Anlage, die den Zähler und alle Einrichtungen umfasst, die erforderlich sind, um
eine korrekte Messung zu gewährleisten, oder dazu dienen, die Messvorgänge zu erleichtern.

## Slide 14
Physikalisch-Technische Bundesanstalt
Braunschweig und Berlin
Bundesallee 100
38116 Braunschweig
Dr.-Ing. Sascha Mäuselein
Arbeitsgruppe „Gesetzliches Messwesen“
Telefon: 0531 592-8310
E-Mail: sascha.maeuselein@ptb.de
www.ptb.de