## Slide 1: OIML Recommendations and Guide with respect to Prepackages Presented by: J Marneweck Convener OIML TC 6

## Slide 2: REALLY? ARE WE DOING ANYTHING NEW
2
Ancient Egypt
Notes: 2
AUTOMATIZACIÓN

## Slide 3
EXAMPLE OF METROLOGY - ANCIENT EGYPT
Standard unit of length – the Cubit
  length of Pharaoh’s forearm plus the width of his palm
Primary standard – in granite
  kept by “Royal Cubit Master”
Working standards
  wooden sticks
Verification/ traceability
  Re-verification of cubit sticks on each full moon
Severe penalty for non-compliance
  Death
Uniformity of length measurement in Egypt had a relative accuracy of 0.05 % over a distance of 230 m

## Slide 4: EXAMLES OF METROLOGY IN TRADE TODAY
  Sale of pre-packed goods – where goods are packed at premises other than the one where the purchase takes place e.g.
    1 kg Flour – packed by mill sold by retail store
    450 ml Beer – Packed by brewery sold in bottle store
    2 l Milk – Packed by dairy sold in retail store
  Sale of goods – where measuring instruments are used to measure the quantity in the presence of the purchaser e.g.
    Meat - sold by a butcher by mass using a scale
    Fuel – sold by a gas station by volume using a liquid fuel dispenser

## Slide 5: EXAMLES OF METROLOGY OF A LEGAL NATURE

## Slide 6: RELATIONSHIP BETWEEN OIML AND THE WTO
OIML is an “international standards-setting organization” in terms of the World Trade Organization’s Technical Barrier to Trade Agreement (WTO TBT Agreement)
OIML Recommendations are considered as international standards in the context of the TBT Agreement
Article 2 of this Agreement states: “Where technical regulations are required and relevant international standards exist or their completion is imminent, Members shall use them, or the relevant parts of them, as a basis for their technical regulations except when such international standards or relevant parts would be an ineffective or inappropriate means for the fulfilment of the legitimate objectives pursued, for instance because of fundamental climatic or geographical factors, or fundamental technological problems.”

## Slide 7: RELATIONSHIP BETWEEN OIML AND THE WTO
This implies that WTO Members should consider OIML Recommendations as the basis for their Legal Metrology legislation where these Recommendations are relevant
Article 2 of the TBT Agreement even encourages WTO Members to participate in appropriate parts of the work of international standard-setting organizations such as the OIML
  With a view to harmonizing technical regulations on as wide a basis as possible, Members shall play a full part, within the limits of their resources, in the preparation by appropriate international standardizing bodies of international standards for products for which they either have adopted, or expect to adopt, technical regulations.

## Slide 8: OIML
The International Organization of Legal Metrology is an intergovernmental treaty organization which:
develops model regulations, standards and related documents for use by legal metrology authorities and industry,
provides mutual recognition systems which reduce trade barriers and costs in a global market,
represents the interests of the legal metrology community within international organizations and forums concerned with metrology, standardization, testing, certification and accreditation,
promotes and facilitates the exchange of knowledge and competencies within the legal metrology community worldwide,
cooperates with other metrology bodies to raise awareness of the contribution that a sound legal metrology infrastructure can make to a modern economy.

## Slide 9: OIML
Notes: 62 Member Countries
64 corresponding Member Countries

## Slide 10: OIML STRUCTURE
International Conference of Legal Metrology
(government delegations)
International Committee of Legal Metrology (CIML)
(government appointed members)
International Bureau of Legal Metrology (BIML)
Presidential Council
Technical work structures
President

## Slide 11: OIML STRUCTURE
International Conference of Legal Metrology
(government delegations)
International Committee of Legal Metrology (CIML)
(government appointed members)
International Bureau of Legal Metrology (BIML)
Presidential Council
Technical work structures
President
Conference meets every four years and set work plans for BIML and CIML

## Slide 12: OIML STRUCTURE
International Conference of Legal Metrology
(government delegations)
International Committee of Legal Metrology (CIML)
(government appointed members)
International Bureau of Legal Metrology (BIML)
Presidential Council
Technical work structures
President
CIML meets yearly to monitor progress of work carried out in previous year and plan for the next year

## Slide 13: OIML STRUCTURE
International Conference of Legal Metrology
(government delegations)
International Committee of Legal Metrology (CIML)
(government appointed members)
International Bureau of Legal Metrology (BIML)
Presidential Council
Technical work structures
President
BIML ensures that technical work is carried out on behalf of CIML and Conference.
Develop model Regulations, facilitate knowledge transfer, cooperate with metrology bodies, represent the interests of the legal metrology authorities, etc.

## Slide 14: OIML STRUCTURE
International Conference of Legal Metrology
(government delegations)
International Committee of Legal Metrology (CIML)
(government appointed members)
International Bureau of Legal Metrology (BIML)
Presidential Council
Technical work structures
President
Technical work is carried out by Technical Committees under the supervision of the BIML

## Slide 15: STRUCTURE OF OIML TECHNICAL WORK
TC 1
TC 2
TC 3
. . .
SC 1
SC 2
SC 3
SC 4
SC 5
TC 4
TC 6
.

## Slide 16: DEVELOPMENT OF INTERNATIONAL STANDARD – STRUCTURE OF OIML WORK
TC 1
TC 2
TC 3
. . .
SC 1
SC 2
SC 3
SC 4
SC 5
TC 4
TC 6
D 13
D 19
D 20
D 27
D 9
D 12
D 18
D 29
D 30
B 3
B 10
p1, p2, p4
p5
p1
p1, p5 p7, p8
p10, p11 p12
V 1
V 2
p2
D 2
D 5
D 8
D 10
D 23
p1, p2, p6
R 34
R 42
D 1
D 3
G 1
p1, p2, p5, p6
.
R 79
R 87
G 21
p3, p5, p6

## Slide 17: DEVELOPMENT OF INTERNATIONAL STANDARD – STRUCTURE OF OIML WORK
Project Group
Convener: Country F
Develops one publication
Part 1
Metrological and technical requirements
Part 2
Test procedures
(for type approval, verification and inspection)
Part 3
Test report format
P-members: A, B, C, D, E, F, G, H
O-members: I, J, K, L
WD
1CD
2CD
3CD ...
WD
1CD
2CD
3CD ...
WD
1CD
2CD
3CD ...

## Slide 18: DEVELOPMENT OF INTERNATIONAL STANDARD – STRUCTURE OF OIML WORK
TC 6 - Prepackaged Product
BIML Contact – Mr Stephen Patoray
Secretariat – South Africa
Convener – Jaco Marneweck
R 79:2015 Labelling requirements for prepackages
R 87:2016 Quantity of product in prepackages
G 21:2017 Guidance for defining the requirements for a certification system for prepackages
  R 87
  G 21

## Slide 19: DEVELOPMENT OF INTERNATIONAL STANDARD – STRUCTURE OF OIML WORK
Member Countries (35) (8)
  Australia, Austria, Belarus, Belgium, Brazil, Canada, Croatia, Cuba, Czech Republic, Denmark, France, Germany, Greece, India, Indonesia, Iran, Japan, Kazakhstan, Korea (R), Netherlands, New Zealand, Norway, PR China, Pakistan, Poland, Serbia, Slovakia, South Africa, Spain, Switzerland, Tunisia, Turkey, UK, USA, Vietnam
Corresponding Member Countries (17) (4)
  Botswana, Bulgaria, Chinese Taipei, Finland, Ireland, Israel, Liberia, Lithuania, Namibia, Romania, Russian Federation, Saudi Arabia, Seychelles, Slovenia, Sweden, Tanzania, UAE
Liaison
  CECIP, CEN, CODEX, European Aerosol Federation, International Federation of Wines and Spirits, IEC, ISO

## Slide 20: DEVELOPMENT OF INTERNATIONAL STANDARD – STRUCTURE OF OIML WORK
CD approved by Project Group
CIML preliminary ballot
CIML approval
Conference sanction
Publication
Five-yearly review

## Slide 21: Requirements for packers with respect to labelling and accuracy requirements for prepackages Presented by: J Marneweck Convener OIML TC 6

## Slide 22: RELAVANT MODEL REGULATIONS
R 79:2015 Labelling requirements for prepackages
R 87:2016 Quantity of product in prepackages
G 21:2017 Guidance for defining the requirements for a certification system for prepackages

## Slide 23: RELAVANT MODEL REGULATIONS
R 79:2015 Labelling requirements for prepackages
R 87:2016 Quantity of product in prepackages
G 21:2017 Guidance for defining the requirements for a certification system for prepackages

## Slide 24: SCOPE - R 79:2015 LABELLING REQUIREMENTS FOR PREPACKAGES
Covers requirements for the labelling of prepackages with respect to:
  Identity of the product
  Declaration of responsibility for a prepackage
  The quantity of product in a prepackage
Applies to prepackages with constant and random nominal quantities
  Does not cover labelling requirements for health, safety, tax or other purposes
  Metrological requirements are given in OIML R 87
  National legislation may exempt prepackages from provisions

## Slide 25: TERMINOLOGY - R 79:2015 LABELLING REQUIREMENTS FOR PREPACKAGES
Revised terminology
  Principal display panel
  Part of the prepackage that is designed to be visible under normal conditions of display for sale
  Note: This is normally the main or front panel of the prepackage and there could be more than one
  The identity of the product should also be marked on the principal display panel

## Slide 26: IDENTITY OF THE PRODUCT
On principle display panel in one of the official languages of the country in which it is offered for sale
Shall be in such type size, font, colour, contrast with background and positioned to make it conspicuous (noticeable), easy to read and understand
Identity shall be in terms of:
  Name specified by national legislation
  Common or usual name by which the product is known
  Generic name

## Slide 27: DECLARATION OF RESPONSIBILITY FOR A PREPACKAGE
Name and complete physical address shall be declared on any surface and positioned to make it conspicuous (noticeable), easy to read and understand in one of the official languages of the country in which it is sold
Name and address of manufacturer or packer may be indicated as code if permitted by national legislation

## Slide 28: QUANTITY DECLARATIONS
On principal display panel
Prepackages not intended for sale need not bear a quantity declaration
How it should be expressed
Presentation of information
  Easy legible boldface print
    Contrasts with background and other information
    Conspicuous (noticeable), easy to read and understand
      Annex B gives examples of possible minimum heights to be used

## Slide 29: MISLEADING PRACTICES
Purchaser not to be misled with respect to the quantity of the product it contains
If purchaser cannot view product it shall be considered to be filled
Slack fill is allowed
Fill level for aerosol dispensers shall be in accordance with national legislation or recognised industry standards
Duplication – If prepackage has more than one principal display panel the product identity and quantity declaration shall appear on each principal display panel in accordance with this Recommendation

## Slide 30: UNITS OF MEASUREMENTS AND SYMBOLS
Units of measurements to be expressed in word or symbols and appropriate symbols are given according to SI system of units
Single space shall be used to separate the number from the unit of measurement
Ambiguous expressions shall not be used as part of quantity declaration
  Approximate
  When packed

## Slide 31: SCOPE – OIML R 87:2016 QUANTITY OF PRODUCT IN PREPACKAGES
Specify legal metrology requirements for prepackaged products in constant nominal quantities
Sampling plans and procedures for use by legal metrology officials in verifying the quantity of product in prepackages

## Slide 32: METROLOGICAL REQUIREMENTS FOR PREPACKAGES
Prepackages shall meet requirements for individual prepackages and average requirement at any level of distribution
Individual requirements
  Actual quantity shall accurately reflect nominal quantity but tolerable deficiencies T shall be allowed
  A homogenous group of prepackages shall contain no more than 2,5 % of packages having T1 errors
  No prepackage shall have T2 error
Average requirement
  Average actual quantity of product shall be at least equal to the nominal quantity
Tolerable deficiencies are specified in Table 1

## Slide 33: 3 Rules
Example: 750 ml beer
prepackage
Test Results
Declared Volume
= 750 ml
Tolerance allowed (T)
= 15ml
Each point on graph represents an actual volume reading

## Slide 34: 3 Rules
Example: 750 ml beer
prepackage
Rule 1
Average must be 750 ml or greater

## Slide 35: 3 Rules
Example: 750 ml Beer
prepackage
Rule 2
The proportion of prepackages that have a negative error greater than TNE (T1 error) shall not be greater than 2,5 % of the batch

## Slide 36: 3 Rules
Example: 750 ml beer
prepackage
Rule 3
No error greater than 2 x TNE allowed
(T2 error)

## Slide 37: REFERENCE TEST FOR METROLOGICAL REQUIREMENTS
General inspection requirements
Control by sampling of inspection lots
  Random sampling, homogeneous (conditions presumed to be uniform),
Statistical principles of control
Lot sizes for inspection purposes
Sampling characteristics
  Sampling plan/s

## Slide 38: ANNEXURES
Annex A – Examination procedure where sampling is used
Annex B – Tare procedures
Annex C – Drained quantity of products packed in a liquid medium
Annex D – Test procedures for determining the actual quantity of frozen products
Annex E – Prohibition of misleading prepackages
Annex F – Basis for statistical sampling model used
Annex G – Schematic representation of the application of T1 and T2 errors
Annex H – Stepwise sampling plan
Annex I – Detailed sampling plans

## Slide 39: SCOPE- OIML G 21:2017 GUIDANCE FOR DEFINING THE REQUIREMENTS FOR A CERTIFICATION SYSTEM FOR PREPACKAGES (GCSP)
Guidance to national authorities on the establishment and maintenance of certification schemes for the control of quantity of product in prepackages and labelling related to the identity of the product, the declaration of responsibility for a prepackage, the quantity declaration and to the certification mark associated with the product

## Slide 40: TERMINOLOGY- OIML G 21:2017 GCSP
Terminology in addition to OIML R 79 and OIML R 87

## Slide 41: GENERAL GUIDANCE
Objectives of certification for prepackages
  Establishing rules and procedures for fostering confidence
  Promoting the efficiency of the control of prepackages whilst facilitating trade
  Promoting harmonization
General principles of a certification system
  Certification system may include one or more scheme
  Generally Government acts as scheme owner and is designating authority
  Public or private bodies may be designated under the scheme
  Depending national legislation participation is voluntary or mandatory
  Mark of conformity may be established to identify prepackages conforming
  Procedures should exist to resolve complaints

## Slide 42: GENERAL GUIDANCE
Content of a certification scheme
  Scope, requirements against which prepackages are evaluated, conformity assessment acivities, requirements the packer must comply with, requirements for designated bodies, etc.

## Slide 43: GENERAL GUIDANCE
Elements for a certification scheme
Scheme elements and activities |  | Different types of certification schemes |  |  |  |  |  | 
 |  | A | B | C | D | E | F | N
4.4.1 | Production system assessment | X | X | X | X | X | X | X
4.4.1.1 | Statement of requirements |  |  |  |  |  |  | 
4.4.1.2 | Application for certification |  |  |  |  |  |  | 
4.4.1.3 | Initial assessment of the production system |  |  |  |  |  |  | 
4.4.1.4 | Review of the evidence of compliance |  |  |  |  |  |  | 
4.4.2 | Certification of the production system | X | X | X | X | X | X | X
4.4.2.1 | Decision on certification |  |  |  |  |  |  | 
4.4.2.2 | Issuing of a certificate |  |  |  |  |  |  | 
4.4.2.3 | Registration of certificates |  |  |  |  |  |  | 
4.4.3 | Licensing |  |  | X | X | X | X | 
4.4.3.1 | Granting the right to use certificates |  |  |  |  |  |  | 
4.4.3.2 | Granting the right to use marks of conformity |  |  |  |  |  |  | 
4.4.4 | Post certification conformity assessment activities |  |  |  |  |  |  | 
4.4.4.1 | Inspection at point of production |  |  | X |  | X | X | 
4.4.4.2 | Inspection in market place |  |  |  | X | X | X | 
4.4.4.3 | Batch licensing |  | X |  |  |  | X | 
4.4.4.4 | Surveillance of the production system |  |  | X | X | X | X | 
Note: “N” has been added to show an undefined number of possible other schemes which can be based on different activities |  |  |  |  |  |  |  | 

## Slide 44: DETAILED GUIDANCE
Minimum requirements for the production system of a packer
Practical examples of different certification schemes
Minimum requirements for designation bodies
Information to be contained in the certificate issued by designated bodies
Design and application of marks of conformity
Resolution of complaints and disputes

## Slide 45: DETAILED GUIDANCE
Minimum requirements for the production system of a packer
  System documentation
  Implementation, maintenance and review of the system
  Competent personnel
  Inspection of packing material
  Retention of records
  Identification of prepackages
  Identification of packing lines
  Measuring instruments
  Sampling and measuring methods
  Non-conforming products

## Slide 46: LEGAL METROLOGY
THANKS FOR LISTENING
QUESTIONS????