## Slide 1
Current Situation of Legislation and C-Mark Scheme for Prepackages in PR China
  Mr. Ma Liqiang
  Senior engineer
  Shenyang Institute of Metrology and Testing, China

## Slide 2
Presently, there are mainly three categories of legal documents for metrological control of prepackages in my economy, which include legislation, standards and regulations (see table1).
Legislation issued by governmental authority aims to facilitate the surveillance of prepackaged products.
Standards and regulations specify the legal metrology requirements for prepackaged products.
Administrative and technical responsibilities for legal metrology in packaging are provided by the above documentation.
Legislation for prepackages

## Slide 3
Legislation for prepackages
Code | Name | Categry
AQSIO 55-2001 | Stipulate of evaluation of metrological assurance competency for prepackages | legislation
AQSIO 106-2001 | Specification of evaluation of metrological assurance competency for prepackages | legislation
AQSIO 75-2005 | Measures of Administration of metrological supervision for prepackages | legislation
JJF 1070-2005 | Rules of metrological inspection for prepackages | regulation
JJF 1070.1-2011 | Rules of metrological inspection for soap products in prepackages | regulation
JJF 1070.2-2011 | Rules of metrological inspection for wheat flour products in prepackages | regulation
GB/T 26993-2011 | Filling and packaging machine for milk powder | standard
Table 1- legal document for prepackages

## Slide 4
Legal metrology control of the prepackages
All the activities of legal metrology control of the prepackaged products are provided as follows:
Categories of prepackaged goods.
Responsibilities of governmental authority on surveillance of prepackages.
Requirements for manufacturers, packers and sellers.
Body designated to perform conformity assessment activities under a certification scheme for prepackages.
Labelling requirements of prepackages.
Sampling requirements and methods of prepackages.
Certification schemes for prepackages.
Design and application of marks of conformity.
Administrative measures for non-conformities.

## Slide 5
JJF 1070-2005 is based on OIML R79-1997 and R87-2004. The regulation is consistent with OIML Recommendations. The regulation mainly specifies：
labelling requirements for prepackages;
metrological requirements for quantity of product in prepackages;
Inspection requirements including examination procedure, expanded uncertainties, statistical principles of control by sampling, lot size for inspection purposes, sampling characteristics, record as well as test report format;
Tare procedures;
Test procedures for determining quantities of mass, volume, linear measure, area, or count.
Regulations for prepackages

## Slide 6
Individual prepackage requirements are as follows:
The actual quantity of product in a prepackage shall accurately reflect the nominal quantity but tolerable deficiencies (T) shall be allowed (Table 4).
A homogenous group of prepackages shall contain no more than 2.5 % of packages having T1 errors.
No prepackage shall have a T2 error.
Individual prepackage requirements

## Slide 7
  Table 4 - Tolerable deficiencies in actual content for prepackages
Tolerable deficiencies for prepackages
Nominal quantity of product (Qn)in g or mL | Tolerable deficiency (T) 1 g or ml | 
 | Percent of Qn | g or ml
0～50 | 9 | ——
50～100 | —— | 4.5
100～200 | 4.5 | ——
200～300 | —— | 9
300～500 | 3 | ——
500～1000 | —— | 15
1000～10000 | 1.5 | ——
10000～15000 | —— | 150
15000～50000 | 1 | ——
1T values are to be rounded up to the next 0.1 of a g or mL for Qn less than or equal to 1 kg or 1L and to the next whole g or mL for Qn higher than 1kg or 1L.

## Slide 8
Tolerable deficiencies for prepackages
Nominal quantity of product (Qn) in length | Percent of Qn
Qn≤5m | No tolerable deficiency allowed
Qn＞5m | Qn×2%
Nominal quantity of product (Qn) in area | Percent of Qn
All Qn | Qn×3%
Nominal quantity of product (Qn) in number | Percent of Qn）
Qn≤50 | No tolerable deficiency allowed
Qn＞50 | Qn×1% 2
  Table 4 (continue)
2 Calculate the value of T by multiplying the nominal quantity by 1 % and rounding the result up to next whole number. The value may be larger than 1 % due to the rounding but this is accepted because the products are whole items and cannot be divided.

## Slide 9
  Average requirements are as follows:
  The average actual quantity of product in prepackages shall be at least equal to the nominal quantity.
  Inspection lot and sampling characteristics is specified in Table 5.
  Number of prepackages in a sample having T1 errors is also provided in Table 5.
  No prepackage shall have a T2 error.
  Table 5 also shows the calculation formula of actual quantity of product in prepackages.
Average requirements for prepackages

## Slide 10
  Table 5 Sampling plans for prepackages
Inspection lot size N | Sample Size n | Correction of average quantity of sample （λ·s） |  | Number of prepackages in a sample with T1 errors
 |  | Sample correction factor λ=t0.995× | Sample standard deviation for actual quantities s | 
1～10 | N | \ | \ | 0
11～50 | 10 | 1.028 | s | 0
51～99 | 13 | 0.848 | s | 1
100～500 | 50 | 0.379 | s | 3
501～3200 | 80 | 0.295 | s | 5
Great then 3200 | 125 | 0.234 | s | 7

## Slide 11
1.The expanded uncertainties (at the k=2 level of confidence) associated with measuring instruments and test methods used for determining quantities shall not exceed 0.2 T.
2.Examples of the source of uncertainty include the maximum permissible error and repeatability in weighing and measuring instruments, variations in packing material and fluctuations in density determinations caused by the differing amounts of solids in the liquid or temperature changes.
3.The informative Annexes of JJF 1070-2005 also include:
  Test procedures for determining the actual quantity of frozen products ;
  Drained quantity of products packed in liquid medium.
Other requirements in the regulations

## Slide 12: 4. The loss of quantity of product after packaging may occur, which is caused by ordinary and customary exposure to environmental conditions in storage and distribution . 5. In this case, it is necessary to draft specific regulation to inspect the particular prepackage. Presently there are two regulations issued by AQSIQ:JJF 1070.1-2011 and JJF 1070.2-2011. 6.The two regulations provide the correction methods for calculating the actual quantity of soap and wheat flour respectively. 7. And the date of production for soap products and moisture contained in the wheat flour are mainly considered.
Other requirements in the Regulations

## Slide 13
Application of c-mark
Once the conformity of the quantity of product in prepackages is certified by governmental authority, the packer will be granted a certificate and a mark of conformity (c-mark) as evidence that the prepackages he produces comply with the stated requirements in legislation.
C-mark identifies prepackages conforming to the legal metrology requirements.
Application of the c-mark of conformity has been subject to national legislation.

## Slide 14
  C-mark is shown in figure 1. The requirements of the c-mark is as follows:
  the mark of conformity is clearly visible to the consumers and not likely to be removed in normal conditions of use.
  c-mark as well as the quantity declaration is presented on prepackaged products.
  the minimum height of figures and characters in the mark should be 3 mm.
Requirements of c-mark
Fig 1 c-mark

## Slide 15
The surveillance procedures for the prepackages have been reformed by AQSIQ as well as some local governmental authorities since 2015.
The reform is based on the development project of the metrology (2013-2020).
The reform of c-mark is also included.
The piloting projects have been conducted in four provinces and a city involving 261 enterprises.
The voluntary use of a mark of conformity on prepackages has been conducted in terms of self declaration of the packers.
Current situation of the reform of c-mark

## Slide 16
The reform of the surveillance procedures for the prepackages aims to:
simplify the surveillance procedures;
improve the efficiency of regulators;
strengthen the post certification conformity assessment activities;
enhance the integrity of the packers;
improve the production processes which will benefit company’s bottom line;
increase the market access of the prepackages;
facilitate the trade of prepackaged goods;
promote the system of credible metrology.
Purpose of the reform of c-mark

## Slide 17
Issues of the reform of c-mark
1.The comparison of present and proposed surveillance procedures is specified in Table 6.
2.The on-site check of the conformity of prepackages and issuing of a certificate have been cancelled.
3. Different software and systems of the surveillance of the conformity of prepackages have been developed, which facilitates both the regulators and the packers.
3. Some issues still need to be solved, which include:
enhance of the impact of c-mark;
participation of the packers;
the revision of the requirements of the c-mark ;
promotion of the mark of conformity.

## Slide 18
Comparison between present and proposed surveillance
Present surveillance procedures | Proposed surveillance procedures
Application for certification by the packers | self declaration of the conformity of prepackages by the manufacturers
On-site check of the conformity of prepackages by governmental authorities | Auditing application documentation of the conformity of prepackages by governmental authorities
Issuing of a certificate | Records of the conformity publicly available on the website
Table 6 comparison between present and proposed surveillance procedures

## Slide 19
Main job of the post surveillance
Main jobs of the post surveillance of the conformity of prepackages in the future include:
strengthen the internal management of the packers;
enhance supervision of the prepackages by the administration;
surveillance of c-mark on website;
periodical inspection of the packaged products;
establishment of the mechanism of reward and punishment.

## Slide 20
Thank you for your kind attention.