## Slide 1
Example of Germany:
Overview about legal metrology control of prepackages
Dr. Peter Ulbig
16 May 2018, Moscow

## Slide 2
Topics of this presentation
Legal framework
Organization
Examples

## Slide 3
How it started in Germany
1935: The law on measures and weights covers the machines for producing prepackages for the first time.
Weighing and filling machines needed to
have a type approval and initial verfication.
Economic growth during the 50s and 60s led to a situation, where PTB was no longer able to do all the type approvals.

## Slide 4
How it started in Germany
1969: The law on metrology and verification covered requirements on prepackages.
Filling capacity of 0.05 to 5 kg or litre for some categories of products (especially foodstuffs)
Specified filling capacities:
50, 100, 125, 200, 250, 500, 1000, 2000, 2500, 3000, 4000 or 5000 grams or millilitres
Baking soda
as a prepackage
around 1960

## Slide 5
The current legal framework
EU-Directive
76/211 EC Prepackages
EU-Directive
98/6 EC Indication of prices of goods
EU-Directive
2007/45 EC Nominal quantities
Measurement
and verifcation act (2013)
By-law on prepackages (1981)
Currently under
revision!

## Slide 6
Legal framework
By-law on prepackages (1981)
What is regulated by the by-law on prepackages?
Labelling of prepackages
Which products have to be labelled by mass and which by volume
Prepackages from 5 g (or ml) to 10 kg (or litre)
Filling quantity of prepackages (requirements)
Ice cream: 850 ml

## Slide 7
Legal framework
The amount within one package
shall not fall below the nominal filling quantity (as the average)
- shall not exceed the fixed values for the minus variation of the nominal filling quantity given by the table
Requirements on the filling quantity for prepackages with the same nominal quantity:
nominal filling quantity QN: | permissable minus variation: | 
in g or ml | in % of QN | in g oder ml
5 bis 50 | 9 | -
50 bis 100 | - | 4,5
100 bis 200 | 4,5 | -
200 bis 300 | - | 9
300 bis 500 | 3 | -
500 bis 1.000 | - | 15
1.000 bis 10.000 | 1,5 | -
equal to 76/211/EEC

## Slide 8
Organization of prepackage control
Measurement and verification act:
§44 no. 8:
„The government may specify the nature and scope of the tests to be performed by the competent public authorities
for monitoring observance of the provisions
enacted on the basis of points …., and regarding the recognition of tests carried out in other States,”

## Slide 9
Organization
16 federal states
13 verification authorities
68 verification offices
1400 verification officers
50 inspectors

## Slide 10
Organization
Control of samples from the shops
Control of filling processes
Activities are mainly planned on the basis of the results of the former years,
complaints of consumers and information from consumer protection agencies

## Slide 11
Examples
Some numbers (given as an average over the past years):
Approx. 20.000 random spot checks/year of prepackages with equal nominal quantity are performed (each check with a number of samples between 8 and 125)
Approx. 70.000 random spot checks/year of prepackages with non-equal nominal quantity are performed

## Slide 12
Examples (equal nominal quantity)
Liquid groceries: 2884 163 5,7 %
non-liquid groceries: 13588 794 5,8 %
Non-groceries: 2856 194 6,8 %
Number of checks:
Failed:

## Slide 13
Examples (equal nominal quantity)
Medicine: 389 12 3,1 %
Length: 26 1 3,8 %
Area: 3 0 0,0 %
Number of checks:
Failed:

## Slide 14
Examples (equal nominal quantity)
Lot size: 166 16 14,3 %
Number of checks:
Failed:

## Slide 15
Examples (non-equal nominal quantity)
Fruits and vegetables: 7101 645 9.1 %
Meat and sausages: 44290 2816 6.4 %
Other foodstuffs: 25571 2238 8,8 %
Number of checks:
Failed:

## Slide 16
Examples
Marking according to the
European Directive 76/211/EEC

## Slide 17
„Bluff packages“
Measurement and verification act:
§43 no. 2:
„(2) It is prohibited to manufacture prepackages, make arrangements for them to be
manufactured, shipped within the territory covered by this Act, put into circulation or
otherwise provide them on the market if the way they are designed and filled mistakenly gives the impression that they contain more than is actually the case.
„bluff packages“:

## Slide 18
„bluff package of the month“
500 g instead of 600 g
price remains the same 2,99 €
equal to 20 % increase
In addition: more sugar, less grain
„bluff package of the month“:
cereals

## Slide 19
Bluff packages of the year

## Slide 20
Physikalisch-Technische Bundesanstalt
Braunschweig und Berlin
Bundesallee 100
38116 Braunschweig
Dr. Peter Ulbig
Head of Division 9 for „Legal and international metrology“
Danke für Ihre Aufmerksamkeit!
Thank you for your attention!
Спасибо за внимание!
感谢您的关注
관심을 가져 주셔서 감사합니다.
شكرا لاهتمامكم